## Slide 1: 68000 Stack-Related Instructions
PEA <EA> Push Effective Address
Calculates an effective address <ea> and pushes it onto the stack pointed at by address register A7 (the stack pointer).
The difference between PEA and LEA
  LEA loads an effective address in any address register.
  PEA pushes it onto the stack.
PEA <EA> is equivalent to:
LEA <EA>,Ai
  MOVEA.L Ai,-(A7)
  Where Ai is an address register other than A7 (A0-A6)

## Slide 2: The MOVE Multiple: MOVEM Instruction
This instruction saves or restores multiple registers.
Useful in subroutines to save the values of registers not used to pass parameters. MOVEM has two forms:
MOVEM register_list,<ea>
MOVEM <ea>,register_list
No effect on CCR
Example: Saving/restoring registers to from memory
SUBR1 MOVEM D0-D7/A0-A6,SAVEBLOCK SAVE D0-D7/A0-A6
. . .
MOVEM SAVEBLOCK,D0-D7/A0-A7 Restore D0-D7/A0-A6
RTS
Example: Saving/restoring registers using the stack (preferred method).
SUBR1 MOVEM D0-D7/A0-A6,-(SP) Push D0-D7/A0-A6 onto the stack
. . .
MOVEM (SP)+,D0-D7/A0-A7 Restore D0-D7/A0-A6 from the stack
RTS

## Slide 3: Example: Power Calculation Subroutine
A subroutine is needed which accepts two integers as input parameters:
  a base, B (a signed integer), Size = one byte (range: -128  B  127)
  an exponent E (a positive integer) Size = one byte,
  and, compute the function BE size of answer = long word
Functional specification (pseudo code) of subroutine POWER:
POWER (B, E)
D1 = B ;input arguments, base
D2 = E ;exponent, a positive integer
initialize D3 to 1 ;answer initialized to 1
while D2 > 0
D3 = D1*D3 ;compute function using
D2 = D2 - 1; ;continued product of base
end POWER
Return to calling program

## Slide 4: Basic Flow Chart of Power
D1 = base
D2 = exponent
D3 = 1
D3 = D3 * D1
D2 = D2 - 1
D2 = 0 ?
No
Yes
Return to
calling program
Word
SP during
subroutine
Initial SP
(and after
return from
subroutine)
Return
address
Effect on The Stack

## Slide 5: POWER: Four Parameter Passing Cases
We’ll examine four assembly versions of subroutine POWER and sample Main programs that calls it.
Each version uses a different parameter passing method:
  Case 1: Parameter passing by value, using data registers.
  Case 2: Parameter passing by reference, using address registers.
  Case 3: Parameter passing by value, using the stack.
  Case 4: Parameter Passing by reference, using the stack

## Slide 6: POWER Subroutine Example (Case 1) Parameter Passing by Value: Using Data Registers - Main Program -
MAIN ORG $400 Main Program origin
MOVEA.L #$07FFE,SP Initialize Stack Pointer
MOVE.B B,D1 Put base number into D1
EXT.W D1 Sign extend base to word length
CLR.W D2 Clear D2 before loading exponent
MOVE.B E,D2 Put exponent number into D2
BSR POWER Call subroutine POWER
LEA A,A5 put address of answer into A5 MOVE.L D3,(A5) save answer
STOP #$2700 Done
ORG $600
B DC.B 4 Base number stored here
E DC.B 2 Exponent number stored here
A DS.L 1 answer to be stored here

## Slide 7: POWER Subroutine Example (Case 1) Parameter Passing by Value: Using Data Registers Continued - Subroutine
ORG $800 Subroutine POWER origin
POWER MOVE.L #1,D3 initialize result to 1
LOOP MULS D1,D3 multiply result with base
SUB #1,D2 decrement power by one
BNE LOOP and repeat as long as power > 0
RTS Done, return to calling program

## Slide 8: POWER Subroutine Example (Case 2) Parameter Passing by Reference: Using Address Registers - Main Program -
MAIN ORG $400 Main Program origin
MOVEA.L #$07FFE,SP Initialize Stack Pointer
LEA B,A1 A1 points to base number
LEA E,A2 A2 points to exponent
BSR POWER Call subroutine POWER
LEA A,A5 put address of answer into A5 MOVE.L D3,(A5) save answer in memory
STOP #$2700 Done
ORG $600
B DC.B 4 Base number stored here
E DC.B 2 Exponent number stored here
A DS.L 1 answer to be stored here

## Slide 9: POWER Subroutine Example (Case 2) Parameter Passing by Reference: Using Address Registers Continued - Subroutine
ORG $800 Subroutine POWER origin
POWER MOVE.B (A1),D1 copy base number to D1
EXT.W D1 Sign extend base to word length
CLR.W D2 Clear D2 before loading exponent
MOVE.B (A2),D2 copy exponent to D2
MOVE.L #1,D3 initialize result in D3 to 1
LOOP MULS D1,D3 multiply result D3 with base D1
SUB #1,D2 decrement power in D2 by one
BNE LOOP and repeat as long as power > 0
RTS Done, return to calling program

## Slide 10: 68000 Addressing Modes Revisited: Address Register Indirect Addressing with Displacement
The addressing notation:
d16(A0) or (d16,A0)
  Refers to the address contained in register A0 plus a signed 16 bit displacement d16
  Some assembles accept only one of the above syntax forms.
Examples:
MOVE.L (12,A4),D3 or MOVE.L 12(A4),D3
MOVE.W (-$4,A1),D0 or MOVE.W -$4(A1),D0

## Slide 11: POWER Subroutine Example (Case 3) Parameter Passing by Value: Using The Stack - Main Program -
MAIN ORG $400 Main Program origin
MOVEA.L #$07FFE,SP Initialize Stack Pointer
MOVE.B B,D1 Put base number into D1
EXT.W D1 Sign extend base to word length
MOVE.W D1,-(SP) push base B onto the stack
CLR.W D2 Clear D2 before loading exponent
MOVE.B E,D2 Put exponent number into D2
MOVE.W D2,-(SP) push exponent E onto the stack
BSR POWER Call subroutine POWER
MOVE.L (SP)+,D3 pop answer from stack resetting SP
LEA A,A5 put address of answer into A5 MOVE.L D3,(A5) save answer
STOP #$2700 Done
ORG $600
B DC.B 4 Base number stored here
E DC.B 2 Exponent number stored here
A DS.L 1 answer to be stored here

## Slide 12: POWER Subroutine Example (Case 3) Parameter Passing by Value: Using The Stack Continued - Subroutine -
ORG $800 Subroutine POWER origin
POWER MOVE.W 6(SP),D1 copy base from stack to D1
CLR.W D2 Clear D2 before loading exponent
MOVE.B 4(SP),D2 copy exponent from to D2
MOVE.L #1,D3 initialize result in D3 to 1
LOOP MULS D1,D3 multiply result D3 with base D1
SUB #1,D2 decrement power in D2 by one
BNE LOOP and repeat as long as power > 0
MOVE.L D3,4(SP) Push result onto the stack
RTS Done, return to calling program

## Slide 13: Effect on The Stack
Word
Just before
calling Subroutine
Current SP
Base B
Exponent E
Initial SP
Word
Just before
end of main
Current SP
= Initial SP
Just after
calling Subroutine
Word
Current SP
Base B
Exponent E
Initial SP
Return
address
8
Word
Just before
return to main
Current SP
Answer
Return
address
Initial SP
4
8
(Case 3)

## Slide 14: POWER Subroutine Example (Case 4) Parameter Passing by Reference: Using The Stack - Main Program -
MAIN ORG $400 Main Program origin
MOVEA.L #$07FFE,SP Initialize Stack Pointer
PEA B Push address of Base onto the stack
PEA E Push address of Exponent onto the stack
PEA A Push address of Answer onto the stack
BSR POWER Call subroutine POWER
LEA 12(SP),SP Stack clean-up: stack pointer reset
STOP #$2700 Done
ORG $600
B DC.B 4 Base number stored here
E DC.B 2 Exponent number stored here
A DS.L 1 answer to be stored here

## Slide 15: POWER Subroutine Example (Case 4) Parameter Passing by Reference: Using The Stack Continued - Subroutine -
ORG $800 Subroutine POWER origin
POWER LEA 12(SP),A1 load Base address in A1
LEA 8(SP),A2 load Exponent address in A2
LEA 4(SP),A3 load Answer address address in A3
MOVE.B (A1),D1 Put base number into D1
EXT.W D1 Sign extend base to word length
CLR.W D2 Clear D2 before loading exponent
MOVE.B (A2),D2 copy exponent from to D2
MOVE.L #1,D3 initialize result in D3 to 1
LOOP MULS D1,D3 multiply result D3 with base D1
SUB #1,D2 decrement power in D2 by one
BNE LOOP and repeat as long as power > 0
MOVE.L D3,(A3) Save result in memory
RTS Done, return to calling program

## Slide 16: Effect on The Stack
Word
Just before
calling Subroutine
Current SP
Initial SP
Base
Address
Exponent
Address
Answer
Address
Word
Just after
calling Subroutine
Current SP
Initial SP
Base
Address
Exponent
Address
Answer
Address
Return
Address
0
+12
+8
+4
(Case 4)
PEA B PEA E
PEA A
BSR POWER

## Slide 17: Effect on The Stack
Just after return
to main
Word
Just after stack
clean-up in Main
Current SP =
Initial SP
Word
Current SP
Initial SP
Base
Address
Exponent
Address
Answer
Address
0
+8
+4
+12
(Case 4)
LEA 12(SP),SP
RTS