## Slide 1: Computer Organization Layers
The computer may be organized into the following layers:
  Application level language
  High level language
  Low level language
  Hardware - may include microcode.
Consider the case of a word processing program:
  The high level commands:
    (save, undo, bold, center, etc.) represent the application level language.
  The high level language might be:
    Pascal, C/C++ or Java.
  The low level language might be:
    68000 or Intel x86 assembler or the proper assembly language for the CPU in use.
I.13

## Slide 2: Basic Assembly Program Structure
Assembly language is made up of two types of statements:
  Executable Instruction:
  One of the processor's valid instructions which can be
  translated into machine code form by the assembler.
  Assembler Directive:
  Inform the assembler about the program and the
  environment and cannot be translated into machine code.
    Link symbolic names to actual values.
    Set up pre-defined constants.
    Allocate storage for data in memory.
    Control the assembly process.
I.14

## Slide 3: Assembler Directives: EQU Directive
The equate directive simply links a name to a value in order to make a program easier to read. It does not reserve space in memory. For example:
  BACK_SP EQU $08
  CAR_RET EQU $0D
The EQU directive may include expressions as well as litrals provided all elements of the expression have already been defined:
  Length EQU 30
  Width EQU 25
  Area EQU Length*Width
I.15

## Slide 4: Assembler Directives: DC Directive
This directive defines a constant and is qualified by:
  .B - to indicate a byte, 8 bits
  .W - to indicate a word, 16 bits
  .L - to indicate a long word, 32 bits
The operand may consist of:
  One or more decimal numbers;
  One or more hexadecimal numbers denoted by a leading '$';
  One or more binary numbers denoted by a a leading '%';
  An ASCII string enclosed in single quotes;
  An expression to be evaluated.
A label in the left hand column equates the label with the first address (word).
The constant is loaded into memory at the current location.
I.16

## Slide 5: Assembler Directives: DS Directive
The define storage directive reserves a storage location in memory but does not store any information.
The directive may be qualified by '.B', '.W' or '.L' to indicate bytes, words or long words.
A operand specifies the number of such quantities to reserve in decimal or hex.
The optional label equates to the address of the first word of storage.
Example:
ORG $1000 Starting address
FIRST DS.B 4 Reserve 4 bytes
SECOND DS.W 4 Reserve 4 words
THIRD DS.L 4 Reserve 4 long words
TABLE DS.W $10 Reserve 16 words
I.17

## Slide 6: Assembler Directives: ORG, END Directives
The origin directive sets up the value of the location counter that tracks where the next item will be stored in memory;
  May be located anywhere in the program.
  Example:
ORG $00001000 Starting address
FIRST DS.B 4 Reserve 4 bytes
ORG $00001100 Change the memory location
SECOND DS.W 4 Reserve 4 words
The end directive indicates that the end of the code has been reached.
  Optionally specifies the place at which to start execution;
  e.g., END $0400.
I.18

## Slide 7: Basic Characteristics of 68000 Assembly Language
An assembly language program line or statement is comprised of the following 4 columns:
  Optional label which must begin in column 1
  An instruction;
    These are the actual instructions themselves, such as MOVE, ADD, etc.
    Opcode fields : The suffixes `.B', `.W', and `.L' denote a byte, word, and long-word operation, respectively. If not specified, the default is word size (.W).
    Basic addressing modes
      Dn data register
      An address register
      #n constant or immediate
      n contents of memory location
  Its operand or operands.
  Optional comment field.
I.19

## Slide 8: Basic Characteristics of 68000 Assembly Language
A line beginning with an asterisk * in the first column is a comment and is totally ignored by the assembler.
Number systems are represented as follows:
  A number without any prefix is decimal.
  A number with a leading '$' is hex.
  A number with a leading '%' is binary.
Enclosing a string in quotes represents a sequence of ASCII characters.
At least one space is required to separate the label and comment field from the instruction; but additional spaces are added for readability.
The following data sizes apply:
  Byte - 8 bits
  Word - 16 bits (default operand size for most instructions).
  Long word - 32 bits
I.20

## Slide 9: Some Basic Assembly Instructions
MOVE D0,Q
MOVE Q,D0
MOVE #Q,D0
ADD Q,D0
ADD D0,Q
CLR Q
CMP Q,D0
CMP #Q,DO
BEQ N
BNE N
BRA N
Copy the contents of register D0 to memory location Q.
Copy the contents of memory location Q to register D0.
Copy the number Q to register D0
Add the contents of memory location Q to register
D0 and put the result in D0.
Add the contents of memory location Q to register
D0 and put the results in memory location Q.
Set the content of memory location Q to zero.
Subtract the contents of memory location Q from the contents
of register D0 in order to set up the CCR. Discard the result
Subtract the number Q from the contents of register
D0 in order to set up the CCR. Discard the result.
Branch to N if the result of the last operation yielded 0.
Branch to N if operands of the last comparison were not equal.
Always branch to location N.
Instruction
Operation Performed
I.21

## Slide 10: 68000 Operand Size and Storage in Memory
The 68000 uses the following suffixes to identify the size of the instruction’s operands:
.B one byte
.W word (2 bytes)
.L long word (4 bytes)
68000 memory is byte-addressed; however, all word and long word operands in memory must start at an even address. For this reason the preferred memory map for 68000 assembly programs show a single word (two bytes) in each row.
When no suffix is specified,
then most instructions
assume .W
When storing values in memory:
The most significant byte is stored
at the first address location
followed by the remaining bytes
Example: Store $AC 35 EF B4
at memory address $1000
Word (16 bits)
$1000 A C 3 5
$1002 E F B 4
Memory Map
I.22

## Slide 11: Example of a Simple Motorola 68000 Assembly Language Program
The following assembly language program adds together the two 8-bit numbers stored in the memory locations called Value1 and Value2, and deposits the sum in Result. Result = Value1 + Value2
ORG $400 Start of program area
MOVE.B Value1,D0
MOVE.B Value2,D1
ADD.B D0,D1
MOVE.B D1,Result
STOP #$2700 Stop execution
ORG $1000 Start of data area
Value1 DC.B 12 Store 12 in memory
Value2 DC.B 24
Result DS.B 1 Reserve a byte for Result
END $400 End of program and entry point
I.23

## Slide 12: Example: Sum Using A Loop
Perform the sum 1 + 2 + 3+...+ 10 by using a loop, or
TOTAL := 0;
FOR COUNTER := 1 TO 10 DO
TOTAL := TOTAL + COUNTER;
This can be solved by the following 68000 Assembler code:
ORG $400 Start of program area
CLR D1 Set the total initially to 0
MOVE.B #1,D0 Initialize the counter to 1
Next ADD.B D0,D1 Add the counter to the total
ADD.B #1,D0 Increment the counter
CMP.B #11,D0 Check if loop is done
BNE Next Go back for another round if not done
STOP #$2700 Stop execution
END
I.24