## Slide 1
68000 CPU and Assembly Language
Introduction 68000.ppt part-I 1-12
I) V.Neumann to 68000
CPU 68000.doc
Registersystem 68000.doc
II) Introduction 68000.ppt part-II 13-24
ggf. Assembler.Introduction.doc
Adressierungstechnik-1.doc
Adressierungstechnik-2.doc
III) Adressing Mode & Instructions.ppt
IV) Arithmetic Instructions.ppt
Subroutines & Stack.ppt
Und VII) ggf. Stack related Instructions & Variables
M. Deutscher-Tiemann
With Selceted Slides from SHAABAN

## Slide 2: Basic computer operation and organization
A computer manipulates binary coded data and responds to events occurring in the external world (users, other devices, network). This is called a stored-program or von-Neumann machine architecture:
  Memory is used to store both programs and data instructions (this is the core of the von-Neumann architecture).
  Program instructions are binary coded data which tell the computer to do something, i.e. add two numbers together.
  Data is simply information to be used by the program, i.e. two numbers to be added together.
  A central processing unit (CPU) with the following tasks:
    Fetching instruction(s) and/or data from memory
    Decoding the instruction(s)
    Performing the indicated sequence of operations
I.1

## Slide 3: The Von-Neumann Computer Model
Partitioning of the computing engine into components:
  Central Processing Unit (CPU): Control Unit (instruction decode , sequencing of operations), Datapath (registers, arithmetic and logic unit, buses).
  Memory: Instruction and operand storage
  Input/Output (I/O)
  The stored program concept: Instructions from an instruction set are fetched from a common memory and executed one at a time
-
Memory
(instructions,
data)
Control
Datapath
registers
ALU, buses
CPU
Computer System
Input
Output
I/O Devices
I.2

## Slide 4: Central Processing Unit (CPU)
Control unit
  Decodes the program instructions.
  Has a program counter which contains the location of the next instruction to be executed.
  Has a status register which monitors the execution of instructions and keeps track of overflows, carries, borrows, etc.
Arithmetic Logic Unit
  Carries out the logic and arithmetic operations as required for instructions decoded by the control unit.
Registers:
  Program counter, status registers, stack pointer for subroutine use.
  A number of general-purpose registers accessed by instructions to store addresses, instruction operands, and ALU results
Control
Unit
Arithmetic Logic
Unit (ALU)
Registers
I.3

## Slide 5: Vertical Grid Organization of Memory
I.4

## Slide 6: Computer Data Storage Units
Bit - Smallest quantity of information that can be manipulated inside a computer; its value is either 0 or 1.
Byte - Defined to be a group of 8 bits; and typically the minimum size required to store a character.
Word - Basic unit of information stored in memory and processed by a computer. Typical computer word lengths are 16, 32 and 64 bits.
For the 68000, a word is 16-bits , and a long word is 32 bits.
Words and long words in the 68000 must start at even memory addresses (e.g. $1000 is allowed, but $1001 produces a memory alignment error).
I.5

## Slide 7: 68000 Architecture
I.6

## Slide 8
68000 Pinout
I.7

## Slide 9: 68000 Register Organization
Data registers
Address registers
Stack pointers
Program counter
Status register
I.8

## Slide 10: Status Register: Condition Code Register
(CCR)
I.9

## Slide 11: Status Register: The System Part
I.10

## Slide 12: Description of 68000 Registers
Program Counter (PC) - points to the next instruction to be executed (24 bits).
General Purpose Registers - D0 through D7
  Called "general purpose" because registers can each perform the same range of functions.
  32 bits wide, but can be divided into 2 words or 4 bytes.
  Bits in the data register have an arbitrary meaning; e.g., two's complement number, unsigned integer, or ASCII characters.
  Word operations applied to these registers can only use the low order 16 bits (d15…d0).
  Byte operations applied to these registers can only use the low order 8 bits (d7…d0).
Address Registers - A0 through A7
  Called "address registers" because they are always used to store the address of a memory location. 32 bits wide, but cannot be subdivided.
  A0 through A6 can be used as you see fit; however, A7 is the stack pointer which is needed to keep track of subroutine return addresses. Therefore, you should not use A7 explicitly.
CCR Register Contains the following flags:
      X eXtend flag (similar to the carry flag)
      N - Negative flag - true if first bit 1 (sign bit or MSB of result is = 1)
      Z Zero flag - true if all bits 0 (result is equal to zero).
      V oVerflow flag (2’s complement overflow)
      C - Carry flag (carry out bit from an arithmetic operation).
    Certain operations effect all bits; e.g., arithmetic. Certain operations effect only some of the
    bits ( e.g., Logical operations do not effect overflow or carry). Certain operations do not effect
    any of the bits (e.g., exchange registers).
I.11

## Slide 13: Computer Instruction Set Architecture (ISA) & Assembly Language
Instruction Set Architecture (ISA) of the Microprocessor:
  Assembly language programmer's view of the processor.
Machine Code:
  CPU language comprised of computer instructions that controls the primitive operations on binary data within the computer, including:
    Data movement and copying instructions
    Arithmetic operations (e.g., addition and subtraction);
    Logic instructions: AND, OR, XOR, shift operations, etc.
    Control instructions: Jumps, Branching,
Assembly Language:
  Human-readable representation of the binary code executed by the computer.
I.12