## Slide 1: 68000 Addressing Modes
Addressing modes are concerned about the way that data is accessed
Addressing can be by actual address or based on a offset from
a known position.
Theoretically, only absolute addressing is required; however, other addressing modes are introduced in order to improve efficiency.
Absolute Addressing:
  Absolute Addressing uses the actual address of an operand;
  either a memory location (e.g., CLR.B $1234) or,
  If a register is involved, this type is also called data register direct, e.g., MOVE.B D2,$2000
Immediate Addressing:
  With Immediate Addressing, the actual operand is part of the instruction; e.g., MOVE.B #25,D2
II.1

## Slide 2: 68000 Addressing Modes
Address Register Indirect Addressing:
  This addressing mode uses the 8 address registers.
  These registers are assumed to contain the address of the data rather than the data itself. e.g. CLR.B (A0)
Address Register Indirect with Post-incrementing:
  A variation of address register indirect in which the operand
  address is incremented after the operation is performed. The syntax is (Ai)+
Address Register Indirect with Pre-decrementing:
  a variation of address register indirect in which the operand is decremented before the operation is performed. The syntax is -(Ai)
II.2

## Slide 3: Address Register Indirect with Post-incrementing / Pre-decrementing
MOVE.B (A0)+,D3 Byte data addressed by A0 are copied to D3. Then
the contents of A0 are incremented by 1.
MOVE.W (A0)+,D3 The word data addressed by A0 are copied to D3.
Then the contents of A0 are incremented by 2.
MOVE.L (A0)+,D3 The long word data addressed by A0 are copied to
D3. Then the contents of A0 are incremented by 4.
MOVE.B -(A0),D3 The address stored in A0 is first decremented by 1.
Then the data addressed are copied to D3.
MOVE.W -(A0),D3 The address stored in A0 is first decremented by 2.
Then the data addressed are copied to D3.
MOVE.L -(A0),D3 The address stored in A0 is first decremented by 4.
Then the data addressed are copied to D3.
Examples
II.3

## Slide 4: Data Movement Instructions
A total of 13 instructions in all: MOVE, MOVEA, MOVE to CCR, MOVE to SR, MOVE from SR, MOVE USP, MOVEM, MOVEQ, MOVEP, LEA, PEA, EXG, SWAP
MOVE copies data from one location to another and may be qualified by ".B" to move 8 bits; ".W" to move 16 bits; and ".L" to move 32 bits.
MOVE does not change the source location only the destination location.
MOVE updates the CCR:
    N Set (=1) if the result (destination) is negative, cleared (=0) otherwise.
    Z Set if the result is zero, cleared otherwise.
    V Always cleared.
    C Always cleared.
    X Not affected.
Examples:
MOVE.B D1,D2 Register to register
MOVE.B D1,1234 Register to memory
MOVE.B 1234,D1 Memory to register
MOVE.B 1234,2000 Memory to memory
MOVE.B #4,D0 Literal to register
MOVE.B #4,1234 Literal to memory
II.4

## Slide 5
II.5

## Slide 6: Data Movement Instructions
MOVEA
Copies a source operand to an address register. May use only
".W” and ".L". In the case of ".W", the source operand is sign
extended. No effect on CCR
  Source Operand: All addressing modes.
  Destination Operand: Address register direct.
Move to CCR
Copies the lower order byte of the operand to the CCR register.
  Source Operand: All except address register direct.
  Destination Operand: CCR register.
EXG
Exchanges the entire 32-bit contents of two registers. Frequently used to
copy an address register to a data register for processing. No effect on CCR.
  Source Operand: Address or data register.
  Destination Operand: Address or data register.
II.6

## Slide 7
II.7

## Slide 8: Data Movement Instructions
SWAP
Exchanges the upper and lower order words of a data register.
  Source Operand: Data register
  Destination Operand: N/A
  CCR set according to resulting register value.
LEA
Copies an effective address into an address register.
  Source Operand:
  All except data register, address register direct, address register
  indirect with pre-decrement or post-increment or immediate.
  Destination Operand: Address register
  No effect on CCR.
II.8

## Slide 9
II.9

## Slide 10: Load Effective Address, LEA Examples
Instruction Action
LEA $0010FFFF,A5 Loads the absolute address
LEA (A0),A5 Loads the contents of another
address register
LEA (12,A0),A5 Loads the contents of an address
register plus a displacement.
LEA (12,A0,D4.L),A5 Loads the contents of an address
register plus a data register plus
a displacement (used for index
addressing).
II.10

## Slide 11: Compare Instructions
All compare instructions subtract the contents of one register (or memory location) from the contents of another register (or memory location) in order to set the CCR (except the X-bit). The results of the subtraction are discarded.
The compare instructions include the following:
CMP Source operand: Any of the addressing modes
Destination: Must be a data register.
CMPA Source operand: Any of the addressing modes
Destination: Must be an address register.
CMPI Source operand is an immediate value
Destination: Any of the addressing modes except address register
direct or immediate.
CMPM Compares one memory location with another
Only addressing mode permitted is address register indirect with
auto- incrementing.
II.11

## Slide 12: Compare Instructions
CMP <source>,<destination>
The compare instruction, CMP <source>,<destination>, subtracts the source operand from the destination operand and updates the bits of the condition code register (CCR), accordingly. The result of the subtraction are discarded.
CMP or other compare instructions is usually followed immediately by a conditional branch (e.g., BEQ branch on zero, BNE branch on zero, BGT branch if greater than, BLT branch if less than, etc). Consider the high-level construct:
MOVE.B X,D0
CMP.B Y,D0 Evaluate X - Y
BGE X_Bigger If X is greater or equal to Y branch
MOVE.B Q,P IF X < Y THEN P = Q
BRA Exit
X_Bigger MOVE.B R,P IF X >= Y THEN P = R
Exit STOP #$2700 Exit point for code-fragment
IF X < Y THEN P = Q
ELSE P = R
II.12

## Slide 13
II.13

## Slide 14
II.14

## Slide 15
II.15

## Slide 16: Conditional Branch Instructions
Identified by mnemonic Bcc where "cc" represents the condition to be checked.
General form: Bcc Address_Label. If the condition is true, then control will branch to "Address_Label".
Mnemonic Instruction Branch Taken If
BNE Branch on not equal Z=0
BEQ Branch on equal Z=1
BPL Branch on not negative N=0
BMI Branch on negative N=1
BCC Branch on carry clear C=0
BCS Branch on carry set C=1
BVC Branch on overflow clear V=0
BVS Branch on overflow set V=1
II.16

## Slide 17: Conditional Branch Instructions For Signed Comparison
Mnemonic Instruction Branch Taken If
BGE Branch on greater than or equal ( N=1 AND V=1)
OR (N = 0 AND V=0)
BGT Branch on greater than (N=1 AND V=1 AND Z=0)
OR (N=0 AND V=0 AND Z=0)
BLE Branch on less than or equal Z=1 OR ( N=1 AND V=0)
OR (N=0 AND V =1)
BLT Branch on less than (N=1 AND V=0)
OR (N=0 AND V=1)
II.17

## Slide 18
Mnemonic Instruction Branch Taken If
BHS, BCC Branch on higher than or equal C=0
BHI Branch on higher than C=0 AND Z=0
BLS Branch on less than or equal C=1 AND Z=1
BLO, BCS Branch on less than C=1
Conditional Branch Instructions For Unsigned Comparison
II.18

## Slide 19: Unconditional Branch Instructions
Two types of unconditional branch instructions:
  BRA Address_Label
  Branches to a statically determined address indicated by
  Address_Label
Examples: BRA START
  BRA EXIT
  JMP
  Jump to an address that can be changed during execution
Examples:
JMP (A0)
JMP D0
II.19

## Slide 20
II.20

## Slide 21: Special Instructions for Address Registers
If an address register is specified as the destination operand, then the following address register instructions:
MOVEA, ADDA, SUBA, CMPA
must be used instead of MOVE, ADD, SUB and CMP,
respectively.
Address instructions only apply to words and long words.
In the case of a word operation, the source operand is sign extended to a long word,
  e.g, $0004 becomes $00000004 and $FFF4 becomes
  $FFFFFFF4.
Address instructions do not change any of the bits of the CCR.
II.21

## Slide 22: Example: Min(X,Y) Using Comparison
* This program demonstrates how to find the smaller of
* two numbers X and Y using the comparison operator.
* if (X <= Y) then
* D0 := X
* else
* D0 := Y
* X and Y are stored in memory and the result of the comparison is stored in
* register D0
ORG $400 Program origin
MOVE.B X,D0 Store X in D0
CMP.B Y,D0 Compare Y and D0
BLE Exit Branch if X <= Y
MOVE.B Y,D0 Otherwise, Y is smaller
Exit STOP #$2700 Halt processor at end of program
ORG $1000
X DC.B 4
Y DC.B 5
END $400
II.22

## Slide 23: Example: Comparing Two Memory Blocks
This program compares two blocks of memory. If the memory is equal, then FF is stored in address register D0, otherwise, 00 is stored.
ORG $400 Program origin
LEA Block1,A0 Point to the beginning of memory block 1
LEA Block2,A1 Point to the beginning of memory block 2
MOVE.W #Size,D0 Store the long word count in size
LOOP CMPM.L (A0)+,(A1)+ Compare the long words
BNE NotEq Branch if not equal
SUBQ.W #1,D0 Otherwise, decrement the count
BNE LOOP Go back for another comparison
CLR.L D0 Two strings are equal so set
MOVE.B #$FF,D0 D0 to FF
BRA Exit
NotEq CLR.L D0 Otherwise, set D0 to 00
Exit STOP #$2700
Size EQU 2 Compare 2 words
ORG $600
Block1 DC.L 'Bloc',’1234' Block 1
ORG $700
Block2 DC.L 'Bloc',’1234 ' Block 2
END $400
II.23

## Slide 24: Example: Reversing a String
This program reverses the contents of a string.
  The address register A0 points to the beginning of the string
  The address register A1 points to the end of the string.
  These pointers move towards each other and swap bytes until the A0 pointer meets or passes A1.
  Register D0 is used for temporary storage.
ORG $400 Program origin
* This section moves the A1 pointer to the end (0 character) of the string
LEA String,A1 Point to the beginning of the string
Loop1 TST.B (A1)+ Move to the end of the string
BNE Loop1 Until the EOS is encountered
SUBA #1,A1 Back up to the EOS
II.24

## Slide 25: Example: Reversing a String (Continued)
* This section swaps the bytes at the opposite ends and moves the
* pointers towards the middle of the string until they meet.
LEA String,A0 Make A0 point to the beginning
Loop2 MOVE.B -(A1),D0 Save the bottom byte
CMP A1,A0 If A0 has reached or passed A1
BHS Exit Then the string is reversed
MOVE.B (A0),(A1) Move the top to the bottom byte
MOVE.B D0,(A0)+ Move the previously saved bottom byte
* to the top byte
BRA Loop2 Loop back for another byte
Exit STOP #$2700
ORG $1000
String DS.B 128 Reserve up to 128 bytes for the string
END $400
II.25