## Slide 1: 68000 Arithmetic Instructions
ADD
Adds the contents of the source location to the contents of a
destination location and stores the result in the destination
location.
  Source: All addressing modes; however, either source or destination must be a data register.
  Destination: All except immediate, address register direct and program relative.
  Effect on CCR flags:
    N Set (=1) if the result (destination) is negative, cleared (=0) otherwise.
    Z Set if the result is zero, cleared otherwise.
    V Set if an overflow is generated, cleared otherwise.
    C Set if a carry is generated, cleared otherwise.
    X Set the same as the carry bit.

## Slide 3: Example: Counting 6’s in An Array
A region of memory starting at location $1000 contains an array of 20 one-byte values.
This program counts the number of 6’s in this array and stores the count in register D1.
ORG $400 Program origin
LEA Array,A0 A0 points to the start of the array
MOVE.B #20,D0 20 values to examine
CLR.B D1 Clear the 6’s counter
Next MOVE.B (A0)+,D2 Pick up an element from the array
CMP.B #6,D2 Is it a 6?
BNE Not_6 IF not 6 THEN skip counter increment
ADD.B #1,D1 IF 6 THEN bump up 6’s counter
Not_6 SUB.B #1,D0 Decrement loop counter
BNE Next Repeat 20 times
STOP #$2700 Halt processor at end of program
ORG $1000
Array DC.B 1,6,4,5,5,6,2,5,6,7,6,6,6,1,3,5,9,6,7,5
END $400

## Slide 4: 68000 Arithmetic Instructions
ADDI
Add immediate: Adds an immediate value to a destination
operand and stores the results in the destination. This can
be used to add an immediate value to a memory location.
  Source: Immediate value.
  Destination: All except address register direct, program counter relative and immediate.
  Effect on CCR flags:
    N Set (=1) if the result (destination) is negative,
    cleared (=0) otherwise.
    Z Set if the result is zero, cleared otherwise.
    V Set if an overflow is generated, cleared otherwise.
    C Set if a carry is generated, cleared otherwise.
    X Set the same as the carry bit.

## Slide 5: 68000 Arithmetic Instructions
ADDX
Adds the contents of the source location and the X flag to the
contents of a destination location and stores the result in the
destination location.
  Source: All addressing modes; however, either source or destination must be a data register.
  Destination: All except immediate, address register direct and program relative.
  Effect on CCR flags:
    N Set (=1) if the result (destination) is negative, cleared (=0) otherwise.
    Z Set if the result is zero, cleared otherwise.
    V Set if an overflow is generated, cleared otherwise.
    C Set if a carry is generated, cleared otherwise.
    X Set the same as the carry bit.

## Slide 6: 68000 Arithmetic Instructions
DIVS, DIVU
DIVU performs unsigned division and DIVS performs signed
division on two's complement numbers.
  The 32-bit long word in the data register is divided by the 16-bit word at the effective address.
  The 16-bit quotient is stored in the lower-order word of the register
and the remainder is stored in the upper-order word.
  Source: All modes except address register direct.
  Destination: Data register.
  Effect on CCR flags:
    N Set if the quotient is negative, cleared otherwise. Undefined if overflow or divide by zero occurs.
    Z Set if quotient is zero, cleared otherwise. Undefined if overflow or divide by zero occurs.
    V Set if division overflow occurs, cleared otherwise. Undefined if overflow or divide by zero occurs.
    C Always cleared.
    X Not affected.

## Slide 7: 68000 Arithmetic Instructions
MULS, MULU
MULU performs unsigned multiplication and MULS performs signed
multiplication on two's complement numbers.
  Multiplication is a 16-bit operation that multiplies the low-order 16-bit word in Dn (destination data register) by the 16-bit word at the effective address. The 32-bit results is stored in Dn.
  Source: All modes except address register direct.
  Destination: Data register.
  Effect on CCR flags:
    N Set if the result is negative, cleared otherwise.
    Z Set if the result is zero, cleared otherwise.
    V Set if an overflow, cleared otherwise.
    C Always cleared.
    X Not affected.

## Slide 8: Sign EXTend Instruction
EXT
Extends the sign bit of the low-order byte or word of a data
register of a data register:
  EXT.W sign extends the low order byte to 16 bits;
  EXT.L sign extends the low order word to 32 bits.
Example:
D0 = $000000C3 Before
EXT.W D0
D0= $0000FFC3 After sign extend
D1 = $0000E1FC Before
EXT.L D1
D0= $FFFFE1FC After sign extend

## Slide 9: Example: Adding Elements of An Array
A region of memory starting at location $1000 contains an array of 10 one-byte signed values (i.e. In 2’s complement representation)
This program adds the elements of this array and stores the sum in register D2 as a long word.
ORG $400 Program origin
LEA Array,A0 A0 points to the start of the array
MOVE.B #10,D0 10 values to add
CLR.B D1 Clear temporary register D1
CLR.L D2 Clear the sum register
Next MOVE.B (A0)+,D1 Copy an element from the array in D1
EXT.W D1 Extend element sign to word size
EXT.L D1 Extend element sign to long word
ADD.L D1,D2 Add array element to the sum in D2
SUB.B #1,D0 Decrement loop counter
BNE Next Repeat 10 times
STOP #$2700 Halt processor at end of program
ORG $1000
Array DC.B $EF,$CD,$CC,$0A,$FF,$DA,$91,$DD,$4A,$8D
END $400

## Slide 10: Arithmetic Shift Left Instruction
The arithmetic shift left operation ASL moves the bits of the operand
the specified number of positions to the left; e.g.,
ASL #3,D0
  Shifts the bits of the D0 register 3 positions to the left.
  This has the effect of multiplying by 2-cubed or 8.
  As each bit is shifted left, it is stored in the Carry flag of the CCR.
  The vacant spot on the right is filled with a zero.
  For example:
[D0] = 00010111 Before
ASL #3,D0
[D0] = 10111000 After

## Slide 11: Arithmetic Shift Right Instruction
The arithmetic shift right operation ASR moves the bits of the operand the
specified number of positions to the right; e.g.,
ASR #3, D0
  Shifts the bits of the D0 register 3 positions to the right.
  This has the effect of dividing by 2 for each position shifted.
  For example:
[ D0] = 00010111 Before
ASR #3, D0
[D0] = 00000010 After
  The bit shifted off the right side is stored in the Carry flag of the CCR.
  On the left side, the MSB is propagated to the left
(also called sign extension). For example:
[D0] = 11101001 Before
ASR #3,D0
[D0] = 11111101 After

## Slide 13: Arithmetic Shift Instructions Operation of ASL, ASR

## Slide 14: Effect of Arithmetic Operations on the CCR: Example
ADD.B SUB.B CLR.B ASL.B ASR.B
Source 01101011 (107) 01101011 (107) 01101011 (107) 01101011 (107) 01101011 (107)
Destination 01011010 (90) 01011010 (90)
( before)
Destination 11000101 11101111 00000000 11010110 00110101
(after)
CCR 0 1 0 1 0 0 1 0 0 0 - 0 1 0 0 0 1 0 1 0 1 0 0 0 1
XNZVC XNZVC XNZVC XNZVC XNZVC

## Slide 15: 68000 Logic Instructions
Logic instructions include:
    AND Bit-wise AND
    ANDI Bit-wise AND with Immediate source
    OR Bit-wise OR
    ORI Bit-wise OR with Immediate source
    EOR Bit-wise Exclusive OR
    EORI Exclusive OR with Immediate source
    NOT 1’s Complement of bits of destination
Effect on CCR:
    X Not affected.
    N Set if the most significant bit of the result is set;
    cleared otherwise.
    Z Set if the result is zero; cleared otherwise.
    V Always cleared.
    C Always cleared.
Examples: AND -(A0),D1 ANDI.B #$CD,D0 ANDI #%00101,CCR
NOT.L D1 OR.L (A1)+ ,D2

## Slide 16: Logical Shift Instructions
LSL / LSR Logical Shift Left/Right
Shifts the operand the specified number of positions left/right;
vacated bit positions are always zero-filled.
  The shift count for the shifting of a register is specified in two different ways:
      Immediate.
      Register: The shift count is the value in the data register specified in the instruction modulo 64.
Effect on CCR:
    X Set according to the last bit shifted out of the operand; unaffected for a shift count of zero.
    N Set if the result is negative; cleared otherwise.
    Z Set if the result is zero; cleared otherwise.
    V Always cleared.
    C Set according to the last bit shifted out of the operand; cleared for a shift count of zero.

## Slide 17: Logical Shift Instructions Operation of LSL, LSR

## Slide 18: Logical Shift Instructions
ROL / ROR Rotate Left/Right
Shifts or rotate the operand the specified number of positions
left/right. Bits that move off one end are put back on the
opposite end after setting or clearing the C-bit.
  The shift count for the shifting of a register is specified in two different ways:
    Immediate.
    Register: The shift count is the value in the data register specified in the instruction modulo 64.
Effect on CCR:
    X Not affected.
    N Set if the most significant bit of the result is set; cleared otherwise.
    Z Set if the result is zero; cleared otherwise.
    V Always cleared.
    C Set according to the last bit rotated out of the operand; cleared
    when the rotate count is zero.

## Slide 19: Rotate Left/Right Instructions : Operation of ROL, ROR

## Slide 20: Logical Shift Operations
ROXL, ROXR Rotate Left/Right with eXtend
Shifts the operand the specified number of positions left/right
including the X-bit.
  Example: ROXR.B #1,D0
    moves bit 7 to 6, bit 6 to 5… bit 1 to 0,
    moves bit 0 to the X-bit and the X-bit to bit 7.
Effect on CCR:
  X Set to the value of the last bit rotated out of the operand;
  unaffected when the rotate count is zero.
  N Set if the most significant bit of the result is set; cleared otherwise.
  Z Set if the result is zero; cleared otherwise.
  V Always cleared.
  C Set according to the last bit rotated out of the operand; when the
    rotate count is zero, set to the value of the extend bit.

## Slide 21: Rotate Left/Right with eXtend Instructions : Operation of ROXL, ROXR

## Slide 22: Example: Setting Parity Bit of A Byte
The following program sets the parity bit (msb) of a byte depending on the number of 1’s in the byte using rotate.
If number of ones is odd parity bit is set( = 1), otherwise = 0
* D0 contains the byte of data whose parity bit is to be set
* D1 contains a temporary working copy of D0
* D2 used to count that 7 bits have been tested
ORG $400 Program origin
MOVE #7,D2 Set the counter to 7
ANDI.B #%01111111,D0 Clear the parity bit to start
MOVE D0,D1 Make a working copy of D0
Next ROR.B #1,D1 Rotate 1 bit right
BCC Zero If the bit is 1 then
EORI.B #%10000000,D0 toggle the parity bit
Zero SUB.B #1,D2 Decrement the counter
BNE Next Check another bit
STOP #$2700
END $400
One Byte
Parity Bit

## Slide 23: Bit Manipulation Instructions
The 68000 four instruction that manipulate single bits:
  BTST Tests the value of a bit. If zero, the Z-flag is set.
  BSET Sets the specified bit to 1.
  BCLR Sets the specified bit to 0.
  BCHG Toggles (reverses) the specified bit.
The bit number for this operation can be specified in one of two ways:
  Immediate: e.g. #0, #1, #2, ...
  Register: The specified data register contains the position of the bit to be manipulated.
Operations are performed on:
  1 bit of a byte if the operand is in memory or
  1 bit of a long word if the operand is a data register. Thus:
  No instruction extension is required.

## Slide 24: Example: Setting Parity Bit of A Byte
The following program sets the parity bit (msb) of a byte depending on the number of 1’s in the byte.
If number of ones is odd parity bit is set( = 1), otherwise = 0
* D0 contains the byte of data whose parity bit is to be set
* D1 contains a counter which will range from 6 to 0
ORG $400 Program origin
MOVE #6,D1 Set the counter to 6
BCLR #7,D0 Clear the parity bit to start
Next BTST D1,D0 Test the bit specified by D1
BEQ Zero If the bit is 1 then toggle parity bit
BCHG #7,D0 toggle the parity bit
Zero SUB.B #1,D1 Decrement the counter
BCC Next Check another bit
STOP #$2700
END $400
One Byte
Parity Bit