## Slide 1: The Stack and Local Subroutine Variables
A Local workspace of size may be required by a subroutine for temporary private variables when there are insufficient registers to handle the calculations.
Recursion involves defining the solution of a problem in terms of itself (i.e a subroutine calling itself).
In order to use the subroutine recursively, this workspace may have to be attached to each use or call of the subroutine.
The stack frame (SF) is defined as a region of temporary storage in memory of size d bytes at the top of the current stack.
Upon creating a frame:
  The frame pointer (FP) points to the bottom of the stack frame. The A6 register is normally used for the frame pointer.
  The stack pointer is updated to point to the top of the frame.
The LINK and UNLK instructions are used to facilitate the creation of local subroutine storage as stack frames.

## Slide 2: Factorials Using Iteration
FactorI MOVE.L D0,-(SP) Save the initial value of D0
MOVE.W D0,D1 Set the result to the input value
Loop SUBQ.W #1,D0 WHILE N > 1
BEQ Exit N := N - 1
MULU D0,D1 Factorial_N := N * Factorial_N
BRA Loop
Exit MOVE.L (SP)+,D0 Restore the value of D0
RTS
Factorial(N)
  If N = 1 THEN
  Factorial(N) := 1
  ELSE
  Factorial(N) := N * Factorial(N-1)
  ENDIF
The factorial of a positive integer is defined as:
  n! = n x (n-1) x (n-2) x (n-3) x .... x 1
Pseudo code:
Assembly Subroutine using iteration:
Computation:

## Slide 3: Factorials Using Recursion
Program to compute the factorial of a number using recursive subroutine
calls. Parameter passing by value via data registers.
ORG $1000
MAIN MOVE.W NUMB,D0 ;get number
JSR FACTOR ;goto factorial routine
MOVE.W D0,F_NUMB ;store result
STOP #$2700
ORG $2000
NUMB DC.W 5 ;number to be factorialized
F_NUMB DS.W 1 ;factorial of number

## Slide 4: Factorials Using Recursion
* Initial conditions: D0.W = number to compute factorial of
* 0 < D0.W < 9
* Final conditions: D0.W = factorial of input number
* Register usage: D0.W destructively used
* Sample case: Input: D0.W = 5
* Output: D0.W = 120
FACTOR MOVE.W D0,-(SP) push input number onto stack
SUBQ.W #1,D0 decrement number
BNE.S F_CONT reached 1 yet?
MOVE.W (SP)+,D0 yes, factorial=1
RTS return
F_CONT JSR FACTOR no, call FACTOR
MULU (SP)+,D0 multiply only after stack
* contains all numbers
RETURN RTS

## Slide 5: Factorials Using Recursion Effect On Stack

## Slide 6: Creating Of A Stack Frame of Size d
Word
Stack just after
a subroutine call
Current SP
A7
Passed
Parameters
Return
Address
Stack just after
creating a stack
frame of size d
in the subroutine
LEA -4(SP),A6
LEA -d(SP),SP
d
Current FP
A6
Passed
Parameters
Return
Address
Current SP
A7
Stack
Frame

## Slide 7: Destroying A Stack Frame
Current FP
A6
Passed
Parameters
Return
Address
Current SP
A7
Stack
Frame
Word
Stack after
destroying the
frame
Current SP
A7
Passed
Parameters
Return
Address
LEA d(SP),SP
d

## Slide 8: LINK
LINK An,-# d
Allocates or creates a frame in the stack for local use by the subroutine of size d bytes.
An is an address register serving as the frame pointer (FP); A6 is used.
Function:
  Push the contents of address register An onto the stack. (includes pre-decrementing SP by 4).
  Save the stack pointer in An (An points to bottom of frame
  Decrement the stack pointer by d (points to the top of the frame)
  Similar in functionality to the following instruction sequence:
  MOVEA.L A6,-(SP)
  LEA (SP),A6
  LEA -d(SP),SP
After creating the frame:
  passed parameters are accessed with a positive displacement with respect to (FP), A6 i.e MOVE.W 8(A6),D0
  Local temporary storage variables are accessed with negative displacement with respect to A6 i.e. MOVE.L D2,-10(A6)

## Slide 9: LINK Instruction Operation
Word
Stack just after
a subroutine call
before LINK
Current SP
A7
Passed
Parameters
Return
Address
Current FP
A6
Passed
Parameters
Return
Address
Current SP
A7
d
Stack
Frame
original
A6
LINK A6,- # d

## Slide 10: UNLINK
UNLINK An
Deallocates or destroys a stack frame. Where An is the address register used as frame pointer (FP); usually A6
Function:
  Restore the stack pointer to the value in address register An
  i.e SP = An or SP = SP +d
  Restore register An by popping its value from the stack.
  (includes post-incrementing SP by 4).
  Similar in functionality to the following instruction sequence:
  LEA d(SP),SP
  MOVEA.L (SP)+,A

## Slide 11: UNLINK Instruction Operation
Current FP
A6
Passed
Parameters
Return
Address
Current SP
A7
d
Stack
Frame
original
A6
Word
Stack just after
UNLINK A6
Current SP
A7
Passed
Parameters
Return
Address
UNLINK A6
A6

## Slide 12: SF Example
MOVE.W D0,-(SP) Push parameter #1 onto stack
MOVE.W D1,-(SP) Push parameter #2 onto stack
JSR SBRT Jump to subroutine SBRT
SBRT LINK A6,-#$8 Establish FP and local storage
. . .
MOVE.W 10(A6),D5 Retrieve parameter #1
. . .
MOVE.W D4,-4(A6) local write to stack frame
. . .
UNLK A6 deallocate stack frame
RTS
A segment of a main program:
A segment of a subroutine:

## Slide 13: SF Example: Effect On Stack
A6
LINK A6,-#$8

## Slide 14: The Effect of Multiple Subroutine Calls on Frame Pointers when Using Local Storage