## Slide 1: Stacks
A stack is a first in, last out (FILO) buffer containing a number of data items usually implemented as a block of n consecutive bytes, words or long words in memory .
In the example below, the stack is composed of words.

## Slide 2: Common Stacks Uses
Data storage:
  This is similar to an array, but is more useful for handling input/output information.
Subroutines calls:
  Before a subroutine is called, the return address (the address of the next instruction of the calling program) is pushed (saved) onto the stack and the stack pointer is adjusted.
Subroutines Returns:
  Upon completion of a subroutine the return address is popped (retrieved) from the stack and loaded in the program counter (PC) and the stack pointer is adjusted.
Subroutine Parameter-Passing:
  Parameters (operands, addresses, etc.) needed by a subroutine may be passed to the subroutine by pushing them onto the stack forming local variables.
  Upon completion such a subroutine all evidence of parameter-passing must be removed from the stack (stack clean-up).

## Slide 3: 68000 Stacks
In the 68000:
Stack addresses begin in high memory ($07FFE for example) and are pushed toward low memory ($07F00 for example).
Other CPUs might do this in the reverse order (grow in high memory).
Normally, address register A7 is used as a main stack pointer in the 68000. Using this register for other addressing purposes may lead to incorrect execution.
68000 main stack item size: One word for data. One long word for addresses.
User-defined stacks that use other item sizes (byte, long word), may be created by using address registers other than A7.

## Slide 4: Initializing The Stack Pointer
It’s the programmer’s responsibility to initialize the stack:
  Initialize the stack pointer: The initial starting address or bottom of the stack.
  Allocate sufficient memory for items to be pushed onto the stack. This could be done by locating the initial stack pointer at a very high memory address.
Example:
INITSP EQU $07FFE Value of INITSP
MOVEA.L #INITSP,A7 Initialize A7
Or …
MOVEA.L #INITSP,SP Initialize SP

## Slide 5: Stack Push, Pop Operations
To push an item onto the stack:
  The stack pointer must be decremented by one word (i.e decremented by 2)
  The word-sized information or data contained in the register or memory location addressed by <source> is put on the stack.
MOVE <source>,-(SP)
To pop an item off the stack:
  The information or data is read from the stack.
  The stack pointer incremented by one word
  The information is put into the register or memory location addressed by <destination>.
  MOVE (SP)+,<destination>
Word
New SP
Old SP
data
Old SP
New SP
data
Push
Pop

## Slide 6: Subroutines Basics
A subroutine is a sequence of, usually, consecutive instructions that carries out a single specific function or a number functions needed by calling programs.
A subroutine can be called from one
or more locations in a program.
Subroutines may be used where the
same set of instructions sequence
would otherwise be repeated in
several places in the program.
Subroutine advantages:
  Make programs more human readable.
  Simplify the code debugging process.

## Slide 7: 68000 Subroutine Calling Instructions
BSR <subroutine_label> Branch to SubRoutine
Where subroutine_label is the address label of the first instruction of the subroutine.
subroutine_label must be within no more than a 16-bit signed offset, i.e. within plus or minus 32K of the BSR instruction.
Does not affect CCR
BSR does the following:
  Pre-decrement the stack
  pointer by 4 (long word)
  Push the program counter,
  (PC) onto the stack.
  Load the program counter
  with the subroutine address
Example:
Main . . .
BSR Subroutine1
. . .
. . .
Stop
Subroutine1 Move …
. . .
. . .

## Slide 8: 68000 Subroutine Calling Instructions
JSR <EA> Jump to SubRoutine
Similar in functionality to BSR, but <EA> must be a memory addressing mode.
i.e. <EA> cannot be a data or address register.
The advantages of this instruction:
  A number of different addressing modes are supported.
  The address of the subroutine can be determined dynamically at execution time
    allows the selection of the subroutine to call at runtime
Does not affect CCR
The most common form used for calling a subroutine.

## Slide 9: 68000 Subroutine Return Instruction
RTS ReTurn from Subroutine
Pops the long word (return address) off of the top of the stack and puts it in the program counter in order to start executing after the point of the subroutine call.
Post increments the stack pointer A7 by 4
Equivalent to the instruction:
JMP (SP)+
Does not affect CCR
Example:
Main . . .
BSR Subroutine1
. . .
. . .
Stop
. . .
Subroutine1 Move …
. . .
. . .
RTS

## Slide 10: Passing Parameters to Subroutines
Parameters may be passed to a subroutine by using:
Memory location:
  This is similar to using static or global data in high level languages.
  Does not produce position independent code and may produce unexpected side effects.
Data and Address Registers:
  Efficient, position-independent.
  It reduces the number of registers available for use by the programmer.
Stack:
  This is the standard, general-purpose approach. May use LINK and UNLK instructions to create and destroy temporary storage on the stack.
  Similar to the approach used by several high-level languages including “C”.

## Slide 11: Two Mechanisms for Passing Parameters
By Value:
  The actual parameter is transferred.
  This is the safest approach unless the parameter needs to be updated.
  Not suitable for large amounts of data.
  In order to pass a parameter by value through the stack, may use the instruction:
MOVE <EA>,-(SP)
By Reference:
  The address of the parameter is transferred.
  This is necessary if the parameter is to be changed
  Recommended in the case of large data volume.
  In order to pass a parameter by reference through the stack, you may use the instruction:
  PEA <EA>